Community Repair Event Safety Guidelines (*.odt)
We're thrilled to have you share your skills at our events. We ask you to remember that Repair Events are learning events, so please work with the owners of broken devices helping them understand and take part in the repair process. Involve them in the repair as much as possible.
Always consider safety and consult with the hosts should you have any questions.
Please read through the safety guidelines below.
Set-up
•	Extension cords must be taped to the floor where possible and kept out of the flow of foot traffic.
•	Soldering. Make sure there is adequate ventilation.
•	Safety items: There is a fire extinguisher ____________, and a first aid kit at ________.
•	Circuit breakers are _______________________________
•	There are exits _________________. They must be kept clear at all times.

Basics
•	Children must be accompanied at all times by an adult responsible for them, and kept an appropriate distance from chemicals, soldering and dangerous tools.
•	Safety glasses must be worn while doing any work involving risk of eye injury.

Electricity **if you have any doubt or question, speak with the hosts.**
•	Power: If you need to plug a device in, test it first.
•	Only repair electric equipment if you are competent to do so.
•	Beware of stored high voltage in switched mode power supplies, even a very long time after it has been unplugged.
•	If you smell burning immediately unplug at the power plug and then assess the problem with a qualified volunteer.
•	Power tools or high-wattage electricals must be assigned to experienced volunteers. If in doubt, ask a host.
•	For any old electrical device, always check that the wiring in the plug is to good standards.
•	If a device has been shorting out electrical circuits, connect the device only after being certain you have found and corrected the problem.
•	No built-in safety features will be bypassed (e.g. fuses, safety switches).
•	Test items after repairs with an eye toward safety.

Aerosol and chemicals
•	Keep them away from any flame or direct sunlight.
•	Be aware of DANGER warnings on labels of chemicals used
•	Do not spray flammable or volatile liquid on a live circuit or close to a soldering iron.
•	Keep chemicals such as solvents far away from other people, especially children.